## Slide 1
Most of the main memory in a general-purpose computer is made up of RAM integrated circuit chips
But a portion of the memory may be constructed with ROM chips.
ROM used for reading only and it is also random access.
ROM is used for storing programs that are permanently resident in the computer and for tables of constants that do not change in value once the production of the computer is completed.
Read-Only Memory (ROM)

## Slide 2
ROM is needed for storing an initial program called a bootstrap loader
The bootstrap loader is a program whose function is start the computer software operating when power is turned on.
The startup of a computer consists of turning the power on and starting the execution of an initial program.
The hardware of the computer sets the program counter to the first address of the bootstrap loader.
Read-Only Memory (ROM)

## Slide 3
The bootstrap program loads a portion of the operating system from disk to main memory and control then transferred to the operating system, which prepares the computer for general use.
The contents of ROM remain unchanged after power is turned off and on again.
Cont’d..

## Slide 4
A ROM is created like any other integrated circuit chip, with the data actually wired into the chip as part of the fabrication process. This presents two problems:
The data insertion step includes a relatively large fixed cost, whether one or thousands of copies of a particular ROM are fabricated.
There is no room for error. If one bit is wrong, the whole batch of ROMs must be thrown out.
Cont’d..

## Slide 5
Programmable ROM (PROM) the PROM is non volatile and may be written into only once
The writing process is performed electrically and may be performed by a supplier or customer.
Variation on read-only memory is the read-mostly memory, which is useful for applications in which read operations are far more frequent than write operations but for which non volatile storage is required.
There are three common forms of read-mostly memory: EPROM, EEPROM, and flash memory.
PROM

## Slide 6
Erasable programmable read-only memory (EPROM)
It is read and written electrically, as with PROM.
Before a write operation, all the storage cells must be erased to the same initial state by exposure of the packaged chip to ultraviolet radiation.
Erasure is performed by shining an intense ultraviolet light through a window that is designed into the memory chip.
EPROM can be altered multiple times
EPROM is more expensive than PROM, but it has the advantage of the multiple update capability.
EPROM

## Slide 7
Electrically erasable programmable read-only memory (EEPROM).
This is a read-mostly memory that can be written into at any time without erasing prior contents; only the byte or bytes addressed are updated.
The write operation takes considerably longer than the read operation, on the order of several hundred microseconds per byte.
The EEPROM combines the advantage of non-volatility with the flexibility of being updatable in place, using ordinary bus control, address, and data lines.
EEPROM is more expensive than EPROM
EEPROM

## Slide 8
First introduced in the mid-1980s
Flash memory is intermediate between EPROM and EEPROM in both cost and functionality.
Flash memory uses an electrical erasing technology.
An entire flash memory can be erased in one or a few seconds which is much faster than EPROM.
It is possible to erase just blocks of memory rather than an entire chip.
Flash memory gets its name because the microchip is organized so that a section of memory cells are erased in a single action or “flash.”
flash memory uses only one transistor per bit.
Flash Memory